## Slide 1: Ethernet MAC

## Slide 2: Introduction for CYT4BF
Ethernet MAC is in the Peripheral blocks:
Review TRM chapter 31 for additional details
Hint Bar

## Slide 3: Ethernet MAC
  Overview
  Ethernet MAC module transmits and receives IEEE802.3 frames
Review TRM chapter 31.1 for additional details
Media Access Control (MAC)
Physical layer (PHY)
Media Independent Interface (MII)
Reduced Media Independent Interface (RMII)
Gigabit Media Independent Interface (GMII)
Reduced Gigabit Media Independent Interface (RGMII)
Management Data Input/Output (MDIO)
Hint Bar
1 RMII is the standard for reducing the number of signals needed to connect the PHY to the MAC than MII.
2 RGMII is the standard for reducing the number of signals needed to connect the PHY to the MAC than GMII.
MII or RMII1 or GMII or RGMII2 and MDIO

## Slide 4: Ethernet MAC Overview
  Features:
  MII, RMII, GMII and RGMII PHY interface
  MDIO interface for PHY management
  10/100/1000 Mbit/s Ethernet MAC compatible with the IEEE 802.3
  Full-duplex communication
  Jumbo frame1 (Max.1536 bytes)
  IEEE 802.1Q: Virtual LAN (VLAN)
  IEEE 802.3: Pause frame
  IEEE 802.1BA: Audio Video Bridging Systems
  IEEE 802.1Qav: Forwarding and Queuing Enhancements for Time-Sensitive Streams
  IEEE 802.1AS: Timing and Synchronization for Time-Sensitive Application in Bridged LAN’s
  IEEE 1588 – Precision Time Protocol
Review TRM chapter 31.1 for additional details
Supports only OPEN Alliance specified RGMII standard
Hint Bar
1 Jumbo frame is not standardized by IEEE.

## Slide 5: Ethernet Frame
Frame format:
  Basic Frame
Review Register TRM for additional details
Start of Frame Delimiter (SFD)
Frame Check Sequence (FCS)
Hint Bar
Preamble
S
F
D
DESTINATION
ADDRESS
SOURCE
ADDRESS
LENG
TH
/
YPE
Payload
46
to
1500
-
octet
FCS
7
-
octet
1
-
octet
6
-
octet
6
-
octet
2
-
octet
4
-
octet

## Slide 6: Ethernet MAC Block Diagram
  Ethernet MAC components:
  MAC Controller
    PHY Interface
    MAC Transmitter/Receiver
    Time Stamp Unit
  TX/RX Packet Mem
  CLK Control
Review TRM chapter 31.2 for additional details
Refer to the Features List in the datasheet for additional details
Hint Bar
MAC Control
AXI
Interface
MMIO
Registers
MII
/
RMII
/
GMII
/
RGMII
and MDIO
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF
5
CLK
_
MEM

## Slide 7: Ethernet MAC Block Diagram
  Ethernet MAC components:
  PHY Interface:
    Supports MII/RMII/GMII/RGMII PHY interface
    Supports MDIO interface
Review TRM chapter 31.3.14 for additional details
Hint Bar
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO

## Slide 8: PHY Interface
  Supports following interface type and transfer rate:
Review TRM chapter 31.3.14 for additional details
Hint Bar
Interface Type | Transfer Rate |  | 
 | 10 Mbit/s | 100 Mbit/s | 1000 Mbit/s
MII |  |  | -
RMII |  |  | -
GMII | - | - | 
RGMII |  |  | 

## Slide 9: MII/RMII/GMII/RGMII Interface
  Supported Signals:
  Transmitter/Receiver signals:
Review TRM chapter 31.3.14 and for additional details
Refer to the Package Pin List and Alternate Functions in the datasheet for additional details
Hint Bar
Pin Name | Function of signals | MII | RMII | GMII | RGMII
TXD[1:0] | Transmit data [1:0] |  |  |  | 
TXD[3:2] | Transmit data [3:2] |  | - |  | 
TXD[7:4] | Transmit data [7:4] | - | - |  | -
TX_CTL | Transmit enable |  |  |  | 
TX_ER | Transmit error |  | - |  | -
TX_CLK | Transmit clock |  | - | - | -
RXD[1:0] | Receive data [1:0] |  |  |  | 
RXD[3:2] | Receive data [3:2] |  | - |  | 
RXD[5:4] | Receive data [7:4] | - | - |  | -
RX_CTL | Receive data valid |  |  |  | 
RX_ER | Receive error |  |  |  | -
RX_CLK | Receive clock |  | - |  | 
REF_CLK | Operation clock out | - |  |  | 
 | Operation clock in | - |  |  | 

## Slide 10: Use case
  MII/RMII Interface:
Review TRM chapter 31.3.14 for additional details
Register info - ETH_CTRL (REFCLK_SRC_SEL)
Hint Bar
Tx and Rx clock source can be supplied from either internal reference clock or from external clock source.
ETH_CTRL register must be used to select the reference clock source from internal reference clock or from HSIO

## Slide 11: Use case
  GMII/RGMII Interface:
Review TRM chapter 31.3.14 for additional details
Register info - ETH_CTRL (REFCLK_SRC_SEL)
Hint Bar
Tx clock source can be selected either from internal clock source or from HSIO
ETH_CTRL register must be used to selects reference clock source from internal reference clock or from HSIO
Tx clock source can be selected either from internal clock source or from HSIO
ETH_CTRL register must be used to selects reference clock source from internal reference clock or from HSIO

## Slide 12: MDIO interface
Review TRM chapter 31.3.12 for additional details
Hint Bar
  Supported Signals:
  MDIO is a single bi-directional tristate signal between the Ethernet MAC and PHY
  MDC is a clock for MDIO
    MDC is generated by dividing CLK_GR4. MDC should not toggle faster than 2.5 MHz (minimum period of 400 ns), as defined by the IEEE 802.3az.
Use case
  ETH_phy_management register is implemented as a shift register. Writing to this register starts a shift operation and outputs to MDIO pin.
Pin Name | Direction | Function of signals
MDIO | IO | Management Data Input/Output
MDC | O | Management Data Clock

## Slide 13: Ethernet MAC Block Diagram
  Ethernet MAC components:
  Clock supplied to EMAC
    For internal operation
      CLK_GR4
      CLK_HF4
      CLK_MEM
      CLK_HF5
Review TRM chapter 31.3.15 for additional details
Hint Bar
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
5
CLK
_
GR
4
CLK
_
HF4
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO

## Slide 14: Clocks to EMAC
  The following clocks are used in Ethernet MAC block functions:
  For internal operation
Review TRM chapter 31.3.15 for additional details
Hint Bar
Clock | Function | Note
CLK_GR4 | Access the register via AHB interface and to support MDIO (MDC clock) | 100 MHz
CLK_HF5 | Time Stamp Unit (TSU) | 200 MHz
CLK_MEM | For AXI operation; DMA | 200 MHz
CLK_HF4 | Internal reference clock for PHY interface | 200 MHz
Clock | Function | Note
CLK_GR4 | Access the register via AHB interface and to support MDIO (MDC clock) | 
CLK_HF5 | Time Stamp Unit (TSU) | 
CLK_MEM | For AXI operation; DMA | 
CLK_HF4 | Internal reference clock for PHY interface | 

## Slide 15: Power Modes
  Ethernet MAC availability in different power modes
Hint Bar
Power Modes | IP Status
Active | Fully operational
LPActive | Fully operational; clocks can be limited to save some power
Sleep | Fully operational
LPSleep | Fully operational; clocks can be limited to save some power
DeepSleep | No clock provided during this mode, hence the logic is not functional. All retention registers will hold the values
Hibernate | Entire EMAC including retention register are not functional

## Slide 16: Ethernet MAC Block Diagram
  Ethernet MAC components:
  EMAC DMA
  MAC Transmitter
  MAC Receiver
  Time Stamp Unit (TSU)
Review TRM chapter 31.3.2 and 31.3.3 for additional details
Hint Bar
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO

## Slide 17: EMAC DMA
  Performs below types of operation
    Receive Buffer Descriptors read/write
    Transmit Buffer Descriptors read/write
    Received data DMA write
    Transmit data DMA read
  Responsible to transfer data between SRAM and EMAC using Packet buffer mode
    8 KB internal transmit packet buffer
    4 KB internal receive packet buffer
  Data Transfer Modes
    Partial Store and Forward Mode
    Full Store and Forward Mode
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 18: Internal Data Path for DMA Packet buffer mode
Review TRM chapter 31.3.2 and 31.3.3 for additional details
Hint Bar

## Slide 19: Tx and Rx Buffer Descriptors
  Configuration parameters for transmit and receive get stored in Buffer Descriptors
  Resides in SRAM
  Memory must be configured as non-cacheable
  Base address for the BDs must be 32 bits aligned
  Depending on Descriptor Time Capture mode, BDs are of
    64 bits when disabled
    128 bits when enabled
  Base address for BD list is pointed by respective queue pointer registers. Such as receive_q_ptr, receive_q1_ptr, transmit_q_ptr
  Allows Ethernet packets to be scattered in the memory
Review TRM chapter 31.3.1.5 and 31.3.1.6 for additional details
Hint Bar

## Slide 20: Tx and Rx Buffer Descriptors
  Buffer Descriptors (BD)
  64/128 bits Transmit BDs
    Buffer Address
    Length
    Checksum offload, CRC, Last buffer
    Used and Last BD
    Status bits
    Time stamp and Errors
  64/128 bits Receive BDs
    Buffer Address
    Ownership and First/Last BD
    Filter match
    Status bits
    SOF and EOF and Length
    Time stamp
Review TRM chapter 31.3.1.5 and 31.3.1.6 for additional details
Hint Bar

## Slide 21: EMAC DMA
Review TRM chapter 31.3.1 for additional details
Hint Bar
  Tx and Rx BDs fetched in advance to enhance the performance
  Upon enabling transmit, buffers are fetched from the highest priority queue’s buffer descriptors, followed by second highest priority queue …. least priority queue
  Tx Packet buffer signals MAC transmitter block to fetch the data depending on the data transfer mode
  Tx Packet buffer continues fetching data until the packet buffer memory is full or maximum limit of 256 packets have reached

## Slide 22: DMA Data Transfer Modes
  Partial Store and Forward Mode
    MAC transmitter starts fetching data from packet buffer when number of available bytes are more than configured watermark level.
      Does not have to wait until entire frame is fetched from external SRAM
    Increases overall system throughput due to less latency time
    Disadvantages:
      Does not allow multi buffer frame
      TCP/UDP checksum offload cannot be used
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 23: DMA Data Transfer Modes
  Full Store and Forward Mode
    Tx Packet buffer waits until entire frame is loaded into the buffer before signaling MAC transmitter block
    Packet buffer holds entire frame until frame is successfully transmitted and status bits are written back to BDs
    During receive process frame only gets forwarded to SRAM when entire frame gets validated
    Triggers overrun error condition when Rx packet buffer is full and no buffer available to store received frame
    Benefits
      No need to fetch entire frame in case transmit error occurs, hence saves AXI transactions
      Doesn’t transfer frame in case of faulty frame received
      Allows multibuffer frames
      Allows usage of IP/TCP/UDP checksum offload feature
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 24: EMAC Transmitter
  Fetches data from packet buffer once packet buffer has enough data
  Start assembling frame by attaching
    Preamble
    Start Frame Delimiter (SFD)
    Payload
    If necessary, adds dummy data to make frame at least of size 60 bytes
    Calculated CRC
    Interframe Gap
Transmits frame using MII/RMII/GMII/RGMII
Updates the statistics register depending on the condition; success/failure/error counters
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 25: EMAC Receiver
  Receives frame and validates
    Correct preamble
    FCS
    Frame length and data alignment
    Based on activated Filter types, received frames either gets written to DMA or not; Filters available such as
    Specific source or destination addresses
    Type ID/Ether Type
    Broadcast enabled/disabled
    Pause frames
    VLAN support enabled/disabled
    Hash addressing
    Copy all frames
Received frame gets forwarded to receive packet buffer and relevant statistics register gets updated
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 26: EMAC Receiver
  Depending on the configured Screener registers, received frame gets written to configured buffer pointed to by Rx BD
  EMAC supports 16 Screening Type 1 and 16 Screening type 2 registers
  Screener Type 1 registers allocates frame based on
    Differentiated services (DS) field of IPv4
    Traffic class (TC) of IPv6
    UDP destination port
  Screener Type 2 registers screens frames based on
    Ether Type
    VLAN Priority
    Field compare register A, B, C
  Unmatched frame gets routed to priority queue 0
Review TRM chapter 31.3.1 for additional details
Hint Bar

## Slide 27: Transmit Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF
5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
Procedure:
  IP Datagrams located in SRAM are transferred to TX Packet Memory using EMAC DMA
1
1

## Slide 28: Transmit Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
Procedure:
  IP Datagrams located in SRAM are transferred to TX Packet Memory using EMAC DMA
  IP Datagram is transferred to MAC Transmitter block
2
1
2
1

## Slide 29: Transmit Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
Procedure:
  IP Datagrams located in SRAM are transferred to TX Packet Memory using EMAC DMA
  IP Datagram is transferred to MAC transmitter block
  Entire MAC frame is constructed by appending preamble, CRC, interframe gap and transmitted by the MAC transmitter block
3
2
3
2
1
1

## Slide 30: Receiver Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
Procedure:
  Incoming MAC frame is verified and filtered by the hardware
1
1

## Slide 31: Receiver Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
MAC Receiver:
  Incoming MAC frame is verified and filtered by the hardware
  Depending on configuration, frame would be forwarded to Rx Packet buffer memory
2
1
1
2
1 Support to DMA transfer. DMAC is implemented in the MAC Control.

## Slide 32: Receiver Flow
MAC Control
AXI
Interface
MMIO
Registers
E
thernet MAC
Clock
Control
PHY Interface
TX
Packet Buff
(
8
K
B
)
RX
Packet Buff
(
4
K
B
)
A
XI master interface
A
HB slave interface
AHB
Interface
AHB
2
APB
MAC Transmitter
MAC Receiver
Time Stamp Unit
(
TSU
)
CLK
_
HF
4
CLK
_
GR
4
CLK
_
HF
5
CLK
_
MEM
MII
/
RMII
/
GMII
/
RGMII
and MDIO
MAC Receiver:
  Incoming MAC frame is verified and filtered by the hardware
  Depending on configuration, frame would be forwarded to Rx Packet buffer memory
  Depending on the filters and configured screening registers, received frame would be written at receive buffer pointed by next available Rx BD
3
2
1
1
2
3

## Slide 33: Pause Frame Support
Pause frame is used to prevent the own self buffer overflow
Review Register TRM for additional details
Priority Flow Control (PFC)
Enhanced Transmission Selection (ETS)
Register info - ETH_network_config - ETH_pause_time
Hint Bar
Fix value
Set to the following register.
- ETH_pause_time
    If enabled, Pause frame can be used to stop transmission for defined time period
    Time is defined in terms of Quanta; 1 Quanta = 512 bits time period

## Slide 34: Pause frame Support
Pause frames to can be transmitted with zero quanta (to resume transmission) or with non-zero quanta time period
If receiving Pause frames enabled, EMAC stops transmission right after receiving non-zero quanta Pause frame
Classical IEEE 802.3 Pause frame:
  Destination address of 0180C2000001h
  A source address taken from Specific Address 1 register
  Type ID of 8808h
  Pause opcode of 0001h
  Pause quantum register
  Padding of 00h to take the frame to minimum frame length
  Valid FCS
Review Register TRM for additional details
Priority Flow Control (PFC)
Enhanced Transmission Selection (ETS)
Register info - ETH_network_config - ETH_pause_time
Hint Bar

## Slide 36: Software Modules

## Slide 37: IP/TCP/UDP Checksum Offloading
  IPv4, TCP and UDP frames have 16 bits checksum included for the payload
  EMAC is capable to generate and verify the checksum for these frame types
  If checksum fails to verify while receiving, frame is discarded, and error counter gets incremented
  For transmit checksum generation occurs only if the frame format is recognized by the MAC, otherwise frame will be sent without checksum and respective status bits get updated.
Review TRM chapter 31.3.5 for additional
Hint Bar

## Slide 38: MAC frame
Frame format:
  Basic Frame
  Q-tagged frame
Review Register TRM for additional details
Start of Frame Delimiter (SFD)
Flag check sequence (FCS)
Hint Bar

## Slide 39: Jumbo Frame Support
The maximum length of Traveo II jumbo frame payload is 1536 bytes
Review Register TRM for additional details
Register Info - ETH_jumbo_max_ length
Hint Bar
MAC CLIENT LENGTH/TYPE
Set to the following register.
- ETH_jumbo_max_length register

## Slide 40: VLAN Support
Provides a virtual LAN group in the network by VLAN tag
VLAN tag is inserted into the Q-tagged frame
Review Register TRM for additional details
Tag Protocol Identifier (TPID)
Tag Control Information (TCI)
Priority Code Point (PCP)
Canonical Format Indicator (CFI)
VLAN identifier (VID)
Register info - ETH_network_config - ETH_stacked_vlan - ETH_dma_config - ETH_screening_type_2 _register_0 to 15
Hint Bar
VLAN Tag
Set to the following register.
- ETH_screening_type_2 _register_0 to 15
Set to the following register.
- ETH_stacked_vlan
Set to the Buffer descriptor.

## Slide 41: Audio Video Bridging Systems Support
Supports the timing and synchronization (IEEE 802.1AS)
Supports the TSU
  Ethernet MAC has a TSU compatible to IEEE 1588
Supports the FQTSS (IEEE 802.1Qav)
  Ethernet MAC has registers to support FQTSS
  FQTSS is controlled by software using registers and supports priority control of transmission data
Review Register TRM for additional details
Time Stamp Unit (TSU)
Forwarding and Queuing Enhancements for Time-Sensitive Streams (FQTSS)
Hint Bar

## Slide 42: Revision History
Revision | ECN | Orig. of Change | Submission Date | Description of Change
** | XXXXXX | SHUS | XX/XX/2018 | Initial release